EV220			Garmin GPS Traverse and Data Collection	Fall 2000

GPS Setup

After turning on the GPS receiver, move to the MENU screen by pressing the PAGE key on the GPS.

Operation Setup

On the MENU page press the down arrow on the keypad to highlight OPERATION SETUP, then press the ENTER key to select.

On the OPERATION SETUP page make sure that the following parameters are selected:

MODE: Normal

OFFSET: -04:00

BACKLIGHT TIME: 0 seconds

TONE: Msg & Key

Press QUIT to exit menu.

Navigation Setup

Select the NAVIGATION SETUP page on the MENU page.

On the NAVIGATION SETUP page select the following parameters:

Position Format:  UTM/UPS

Map Datum: NAD27CONUS

CDI Scale: +/- 0.25

UNITS: Metric

HEADING: True

Press the QUIT key to exit the menu

Track Log Setup

Select the TRACK LOG SETUP on the MENU page

On the TRACK LOG SETUP Page select the following parameters:

RECORD TRACK: No

CRITERIA: Automatic

CLEAR TRACK LOG? Yes (if memory used is not equal to 0%)

Press the QUIT key to exit.

Map Setup

Select the MAP SETUP from the MENU page.

On the MAP SETUP page select the following parameters:

ORIENTATION: North Up

PLOTTED ITEMS:

RINGS: Yes

ROUTE: Yes

NEAREST: Yes

NAMES: Yes

TRACK LOG: 50

- Press the QUIT key to exit.