EV220	Trimble GeoExplorer Data Dictionary		Fall 2000

Creating a Data Dictionary

- Complete the Data Dictionary Tutorial in Chapters 3 and 4 Pathfinder Software Volume 2.  As additional reference, Chapter 2 provides an overview of Data Dictionaries.

- After completing the Data Dictionary Tutorial exercise, review the types of features that you represented on your traverse. Create a Data Dictionary Outline on the accompanying form with suitable feature names, attribute names and attribute values. Remember that when constructing the Data Dictionary, you will have to identify the attribute type (numeric, text, date, etc.).

- Ensure that you add line and area features to the data dictionary. A typical line feature could be the sidewalks cutting across your traverse area; an area feature would be the traverse area.

Example of Data Dictionary Outline

| Feature | Feature Name | Attribute Name | Attribute Value |
| --- | --- | --- | --- |
| Point (point) | Power Pole | Material | Wood |
|  |  |  | Metal |
|  |  |  | Concrete |
|  |  | Height |  |
| Line (polyline) | Walkway | Surface Type | Gravel |
|  |  |  | Natural |
|  |  |  | Concrete |
| Area (polygon) | Traverse Area | Name |  |
| Area (polygon) | Parking Lot | Surface Type | Asphalt |
|  |  |  | Concrete |
|  |  |  | Turf |
|  |  | Name |  |

- After creating the Data Dictionary, transfer the Data Dictionary to the Trimble GeoExplorer following the instructions on handout 4.2.1 Transferring a Data Dictionary.

- To record features follow the instructions on handout 5.5 Recording Files with a Data Dictionary.

EV220	Trimble GeoExplorer Data Dictionary Outline	Fall 2000

Crew:

_______________________	________________________	Date:_______________________

| Feature | Feature Name | Attribute Name | Attribute Value |
| --- | --- | --- | --- |